## Slide 1: EETS 8355: data center network engineering
Dr. M. Scott Kingsley
Virtual Extensible LAN (VXLAN)

## Slide 2: DATA CENTER OVERLAY EVOLUTION
Cisco
ACI
VXLAN/BGP
/EVPN
Figure 1: Data Center Overlay Evolution

## Slide 3: VXLAN OVERVIEW
Traditional network segmentation has been provided by VLANs that are standardized under the IEEE 802.1Q group.
VLANs provide logical segmentation of Layer 2 boundaries or broadcast domains.
However, due to the inefficient use of available network links with VLAN use, rigid requirements on device placements in the data center network, and the limited scalability to a maximum 4094 VLANs, using VLANs has become a limiting factor to IT departments and cloud providers as they build large multitenant data centers.

## Slide 4: VXLAN OVERVIEW
Cisco, in partnership with other leading vendors, proposed the Virtual Extensible LAN (VXLAN) standard to the IETF as a solution to the data center network challenges posed by traditional VLAN technology.
The VXLAN standard provides for the elastic workload placement and higher scalability of Layer2 segmentation that is required by today’s application demands.
VXLAN Overview: Cisco Nexus 9000 Series Switches

## Slide 5: VXLAN OVERVIEW
Cisco Nexus 9000 Series Switches can run in ACI mode or NX-OS mode. In ACI mode Cisco Nexus 9000 Series Switches when used in combination with the Cisco Application Policy Infrastructure Controller (APIC) provide an application centric infrastructure.
In NX-OS mode Cisco Nexus 9000 Series Switches function as classic switches.
The VXLAN implementations on Cisco Nexus 9000 Series switches differ between ACI mode and NX-OS mode. This is an overview of VXLAN on Cisco Nexus 9000 Series Switches in NX-OS mode.

## Slide 6: VXLAN OVERVIEW
As its name indicates, VXLAN is designed to provide the same Ethernet Layer 2 network services as VLAN does today, but with greater extensibility and flexibility. Compared to VLAN, VXLAN offers the following benefits:
  Flexible placement of multitenant segments throughout the data center: It provides a solution to extend Layer 2 segments over the underlying shared network infrastructure so that tenant workload can be placed across physical pods in the data center.

## Slide 7: VXLAN OVERVIEW
  Higher scalability to address more Layer 2 segments: VLANs use a 12-bit VLAN ID to address Layer 2 segments, which results in limiting scalability of only 4094 VLANs. VXLAN uses a 24-bit segment ID known as the VXLAN network identifier (VNID), which enables up to 16 million VXLAN segments to coexist in the same administrative domain.

## Slide 8: VXLAN OVERVIEW
  Better utilization of available network paths in the underlying infrastructure: VLAN uses the Spanning Tree Protocol for loop prevention, which ends up not using half of the network links in a network by blocking redundant paths.
  In contrast, VXLAN packets are transferred through the underlying network based on its Layer 3 header and can take complete advantage of Layer 3 routing, equal-cost multipath (ECMP) routing, and link aggregation protocols to use all available paths.

## Slide 9: VXLAN ENCAPSULATION AND PACKET FORMAT
VXLAN is a Layer 2 overlay scheme over a Layer 3 network.
It uses MAC Address-in-User Datagram Protocol (MAC-in-UDP) encapsulation to provide a means to extend Layer 2 segments across the data center network.
VXLAN is a solution to support a flexible, large-scale multitenant environment over a shared common physical infrastructure.

## Slide 10: VXLAN ENCAPSULATION AND PACKET FORMAT
The transport protocol over the physical data center network is IP plus UDP.
VXLAN defines a MAC-in-UDP encapsulation scheme where the original Layer 2 frame has a VXLAN header added and is then placed in a UDP-IP packet.
With this MAC-in-UDP encapsulation, VXLAN tunnels Layer 2 network over Layer 3 network.
The VXLAN packet format is shown in Figure 2.

## Slide 11: VXLAN ENCAPSULATION AND PACKET FORMAT
VXLAN uses VXLAN tunnel endpoint (VTEP) devices to map tenants’ end devices to VXLAN segments and to perform VXLAN encapsulation and de-encapsulation.
Each VTEP function has two interfaces:
  One is a switch interface on the local LAN segment to support local endpoint communication through bridging.
  The other is an IP interface to the transport IP network.

## Slide 12: VXLAN ENCAPSULATION AND PACKET FORMAT
The IP interface has a unique IP address that identifies the VTEP device on the transport IP network known as the infrastructure VLAN.
The VTEP device uses this IP address to encapsulate Ethernet frames and transmits the encapsulated packets to the transport network through the IP interface.

## Slide 13: VXLAN TUNNEL ENDPOINT (VTEP)
A VTEP device also discovers the remote VTEPs for its VXLAN segments and learns remote MAC Address-to-VTEP mappings through its IP interface.
The functional components of VTEPs and the logical topology that is created for Layer 2 connectivity across the transport IP network is shown in Figure 2 on the next slide.

## Slide 14: VXLAN TUNNEL ENDPOINT (VTEP)
Figure 2: VTEP Functionality

## Slide 15: VXLAN TUNNEL ENDPOINT (VTEP)
The VXLAN segments are independent of the underlying network topology; conversely, the underlying IP network between VTEPs is independent of the VXLAN overlay.
It routes the encapsulated packets based on the outer IP address header, which has the initiating VTEP as the source IP address and the terminating VTEP as the destination IP address (Figures 3 and 4).

## Slide 16: VXLAN ENCAPSULATION AND PACKET FORMAT
Figure 3: VXLAN Encapsulation

## Slide 17: VXLAN ENCAPSULATION AND PACKET FORMAT
Figure 4: VXLAN Encapsulation Detail

## Slide 18: Homework
Header format
https://www.youtube.com/watch?v=jjr8aIIRkYc&list=PLDQaRcbiSnqFe6pyaSy-Hwj8XRFPgZ5h8&index=2