## Slide 1: EETS 8355: data center network engineering
Dr. M. Scott Kingsley
Virtual Extensible LAN (VXLAN) 2

## Slide 2: VXLAN PACKET FORWARDING
As previously illustrated, VXLAN introduces an 8-byte VXLAN header that consists of a 24-bit VNID and a few reserved bits.
The VXLAN header together with the original Ethernet frame goes in the UDP payload.
The 24-bit VNID is used to identify Layer 2 segments and to maintain Layer 2 isolation between the segments.
With all 24 bits in VNID, VXLAN can support 16 million LAN segments.
Figure 5 on the following slide and related explanation demonstrate how VXLAN packets are forwarded and processed.

## Slide 3: VXLAN PACKET FORWARDING
Figure 5: VLAN Packet Forwarding Illustrated

## Slide 4: VXLAN PACKET FORWARDING
In the VXLAN Packet Forwarding diagram on the previous slide, Host-A and Host-B in VXLAN segment 10 communicate with each other through the VXLAN tunnel between VTEP-1 and VTEP-2.
This example assumes that address learning has been done on both sides, and corresponding MAC-to-VTEP mappings exist on both VTEPs.

## Slide 5: VXLAN PACKET FORWARDING
Host-A and Host-B in VXLAN segment 10 communicate with each other through the VXLAN tunnel between VTEP-1 and VTEP-2.
This example assumes that address learning has been done on both sides, and corresponding MAC-to-VTEP mappings exist on both VTEPs.

## Slide 6: VXLAN PACKET FORWARDING
When Host-A sends traffic to Host-B, it forms Ethernet frames with MAC-B address of Host-B as the destination MAC address and sends them out to VTEP-1.

## Slide 7: VXLAN PACKET FORWARDING
VTEP-1, with a mapping of MAC-B to VTEP-2 in its mapping table, performs VXLAN encapsulation on the packets by adding VXLAN, UDP, and outer IP address header to it. In the outer IP address header, the source IP address is the IP address of VTEP-1, and the destination IP address is the IP address of VTEP-2.
  VTEP-1 then performs an IP address lookup for the IP
  address of VTEP-2 to resolve the next hop in the transit
  network and subsequently uses the MAC address of the
  next-hop device to further encapsulate the packets in an
  Ethernet frame to send to the next-hop device.

## Slide 8: VXLAN PACKET FORWARDING
Which subsequently uses the MAC address of the next-hop device to further encapsulate the packets in an Ethernet frame to send to the next-hop device.
The packets are routed toward VTEP-2 through the transport network based on their outer IP address header, which has the IP address of VTEP-2 as the destination address.
After VTEP-2 receives the packets, it strips off the outer Ethernet, IP, UDP, and VXLAN headers, and forwards the packets to Host-B, based on the original destination MAC address in the Ethernet frame.

## Slide 9: VXLAN FOR BUM
VXLAN on Cisco Nexus 9000 Series Switches uses existing Layer 2 mechanisms - flooding, and dynamic MAC address learning - to do the following:
  Transport broadcast, unknown unicast, and multicast traffic
  Discover remote VTEPs
  Learn remote host MAC addresses and MAC-to-VTEP mappings for each VXLAN segment
For these traffic types, IP multicast is used to reduce the flooding scope of the set of hosts that are participating in the VXLAN segment.

## Slide 10: VXLAN FOR BUM
Each VXLAN segment, or VNID, is mapped to an IP multicast group in the transport IP network.
Each VTEP device is independently configured and joins this multicast group as an IP host through the Internet Group Management Protocol (IGMP).
The IGMP joins trigger Protocol Independent Multicast (PIM) joins and signaling through the transport network for the particular multicast group.
The multicast distribution tree for this group is built through the transport network based on the locations of participating VTEPs. The multicast tunnel of a VXLAN segment through the underlying IP network is shown in Figure 6.

## Slide 11: VXLAN FOR BUM
Figure 6: VXLAN using a multicast group

## Slide 12: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
This multicast group is used to transmit VXLAN broadcast, unknown unicast, and multicast traffic through the IP network, limiting Layer 2 flooding to those devices that have end systems participating in the same VXLAN segment.
VTEPs communicate with one another through the flooded or multicast traffic in this multicast group.

## Slide 13: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
The Cisco Nexus 9000 VXLAN implementation uses the classic Layer 2 data plane flooding and learning mechanisms for remote VTEP discovery and tenant address learning.
The tenant VXLAN segment has VNID 10 and uses the multicast group 239.1.1.1 over the transport network.
It has three participating VTEPs in the data center.
Assume that no address learning has been performed between locations.
End System A (with IP-A, MAC-A) starts IP communication with End System B (with IP-B, MAC-B). The sequence of steps is shown in Figure 7.

## Slide 14: REMOTE VTEP DISCOVERY AND ADDRESS LEARNING
Figure 7: REMOTE VTEP DISCOVERY AND ADDRESS LEARNING

## Slide 15: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
End System A sends out an Address Resolution Protocol (ARP) request for IP-B on its Layer 2 VXLAN network.
VTEP-1 receives the ARP request. It does not yet have a mapping for IP-B. VTEP-1 encapsulates the ARP request in an IP multicast packet and forwards it to the VXLAN multicast group. The encapsulated multicast packet has the IP address of VTEP-1 as the source IP address and the VXLAN multicast group address as the destination IP address.

## Slide 16: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
The IP multicast packet is distributed to all members in the tree. VTEP-2 and VTEP-3 receive the encapsulated multicast packet because they’ve joined the VXLAN multicast group. They de-encapsulate the packet and check its VNID in the VXLAN header. If it matches their configured VXLAN segment VNID, they forward the ARP request to their local VXLAN network. They also learn the IP address of VTEP-1 from the outer IP address header and inspect the packet to learn the MAC address of End System A, placing this mapping in the local table.
VXLAN Oerview: Cisco Nexus 9000 Series Switches

## Slide 17: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
End System B receives the ARP request forwarded by VTEP-2. It responds with its own MAC address (MAC-B), and learns the IP-A-to-MAC-A mapping.
VTEP-2 receives the ARP reply of End System B that has MAC-A as the destination MAC address. It now knows about MAC-A-to-IP-1 mapping. It can use the unicast tunnel to forward the ARP reply back to VTEP-1. In the encapsulated unicast packet, the source IP address is IP-2 and the destination IP address is IP-1. The ARP reply is encapsulated in the UDP payload.

## Slide 18: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
VTEP-1 receives the encapsulated ARP reply from VTEP-2. It de-encapsulates and forwards the ARP reply to End System A. It also learns the IP address of VTEP-2 from the outer IP address header and inspects the original packet to learn MAC-B-to-IP-2 mapping.
Subsequent IP packets between End Systems A and B are unicast forwarded, based on the mapping information on VTEP-1 and VTEP-2, using the VXLAN tunnel between them.

## Slide 19: REMOTE VTEP DISCOVERY AND REMOTE ADDRESS LEARNING
https://www.youtube.com/watch?v=QPqVtguOz4w

## Slide 20: VXLAN WITH WIRESHARK
https://www.youtube.com/watch?v=Jqm_4TMmQz8