## Slide 1: EETS 8355: data center network engineering
Dr. M. Scott Kingsley
NETWORK DISAGGREGATION

## Slide 2: Network Disaggregation
Network Disaggregation defines the evolution of switching and routing appliances from proprietary, closed hardware and software sourced from a single vendor, towards totally decoupled, open components which are combined to form a complete switching and routing device.

## Slide 3: AT&T Network Transformation
Network growth necessitates economies of scale that can only be achieved from interoperability and open disaggregation.
  The open dNOS, like AT&T’s Vyatta NOS, that’s disaggregated from the underlying hardware (chassis, controller, line cards, etc.).
  Well-defined standard interfaces and APIs enabling modularity with the ability to mix and match applications.
  Independent scaling of control and user/data plane functions to drive an open ecosystem.
  AT&T is leading efforts in industry bodies like the Open Compute Project (OCP), Open Networking Foundation (ONF), Open-RAN (O-RAN), OpenROADM, and the Linux Foundation to commoditize interoperable network functions and compute modularity without being cost prohibitive.
https://about.att.com/content/dam/snrdocs/7_Tenets_of_ATTs_Network_Transformation_White_Paper.pdf

## Slide 4: Traditional server components

## Slide 5: Disaggregation
Silicon
Operating system
Original Device Manufacturers (ODM’s)
White vs. Grey vs. Brite boxes
Routing stacks
Standards and foundations

## Slide 6: Disaggregation

## Slide 7: Silicon
Data center operators want larger port count switches to build large networks they also want smaller port count switches for each leaf.
Silicon vendors provide two (or more) variations: one for spines and one for leafs.
Cisco, Juniper
“Merchant” silicon
  Broadcom Trident and Tomahawk
Programmable chipsets

## Slide 8: Silicon
Throughput
  12.8 Tbps
  25.6 Tbps
Port speed examples
  48 x 1/10/25 GbE
  32 x 400 GbE
  64 x 200 GbE
  16 x 100 GbE
  64 x 100 GbE

## Slide 10: Silicon
AMD
Intel
NVIDIA
ARM
  AWS
  Google
  Microsoft
Broadcom
Barefoot
Innovium

## Slide 11: Network Operating Systems
Cumulus Networks Linux
Big Switch Switch Light
Open Network Linux
Dell Systems FTOS
IPinFusion OcNos
Coriant NOS
Arista Networks EOS
Facebook FBOSS
Microsoft Cloud SONIC (Azure Cloud Switch)
VYOS (formerly Vyatta)
ONOS
More……

## Slide 12: Rise of the ODM’s

## Slide 13: End of lecture 2

## Slide 14: NVIDIA
The Data Center is the New Unit of Computing (NVIDIA GTC 2021 Keynote Part 3) – YouTube

## Slide 15: ODM’s
DNI
Supermicro
Edgecore
Quanta
Celestica

## Slide 16: White box versus Brite box

## Slide 17: White box versus Brite box
White box switch
  White box switch is a by-product of SDN, which decouples the hardware (a bare metal switch) from the NOS.
  It allows customers to buy open switch hardware and pair it with their preferred networking operating system (NOS) like Cumulus Linux or PicOS. Customers can buy white box switch from hardware suppliers like Accton, Quanta.
Brite box switch
  The term “brite box” is a white box switch but with a brand name such as Dell and HP on them.
  A brite box switch is the middle ground between a traditional switch and white box switch.
  Brite box switches are pre-loaded with a vendor’s (e.g. Cumulus Networks or Big Switch Networks) operating system.
  Thus, using brite box switch, customers can receive professional service from the hardware and software suppliers.
  As an open source switch, it allows customers to have the flexibility to choose the switch software.

## Slide 18: Empire Strikes Back
Cisco ACI
Intent-based networking

## Slide 19: Standards and foundations
Open Compute Project
Open Network Foundation (Openflow and SDN)
Linux Foundation
IETF
IEEE

## Slide 20: Routing stacks
Every vendor has at least one
  Feature rich
  High performance
  Proprietary
Reasons for using something else:
  Vertical integration with some operating system
  Customization or tuning to fit needs

## Slide 21: Routing Stacks: FRRouting
FRRouting (FRR) is a free and open source Internet routing protocol suite for Linux and Unix platforms.
It implements BGP, OSPF, RIP, IS-IS, PIM, LDP, BFD, Babel, PBR, OpenFabric and VRRP, with alpha support for EIGRP and NHRP.
FRR’s seamless integration with native Linux/Unix IP networking stacks makes it a general purpose routing stack applicable to a wide variety of use cases including connecting hosts/VMs/containers to the network, advertising network services, LAN switching and routing, Internet access routers, and Internet peering.

## Slide 22: FRRouting

## Slide 23: Disaggregation participants

## Slide 24: SMU/AT&T Virtualization Center

## Slide 25: YouTube
Facebook's Data Center Fabric
  www.youtube.com/watch?v=kcI3fGEait0&t=1888s
  https://www.youtube.com/watch?v=KKIVEj-YbiU&t=682s
Google data center
  https://www.youtube.com/watch?v=pIZXvVl8vIM
  https://www.youtube.com/watch?v=7ygRSyeizPw&t=492s
  https://www.youtube.com/watch?v=eE-8VXB1xUo&t=1648s

## Slide 26: YouTube
The link below goes with the linear programming lecture:
Moving Fast with Facebook's New Long-Haul Network - Facebook - Network@Scale2017
  https://www.youtube.com/watch?v=PeqaVCDRDY4

## Slide 27: YouTube
GOOGLE DATA CENTER 2021
  https://www.youtube.com/watch?v=kythGOICErQ