## Slide 1
TECHNICAL COMPARISON SERIES
Server Virtualization Technologies
A comparative analysis of DPDK, SR-IOV, and VMDq — three approaches to eliminating kernel and hypervisor overhead in high-performance virtualized networking.
Data Center & NFV Performance Engineering · February 2026
01 / 15
DPDK — Data Plane Development Kit
Open-source kernel-bypass framework. Moves packet processing into user space using Poll Mode Drivers. Eliminates interrupts and context switching. Best for East-West intra-server traffic.
SR-IOV — Single Root I/O Virtualization
PCI-SIG hardware standard. Partitions a NIC into Virtual Functions assigned directly to VMs. Bypasses the hypervisor vSwitch entirely via IOMMU DMA. Best for North-South inter-server traffic.
VMDq — Virtual Machine Device Queues
Intel hardware-assist offload. Assigns per-VM hardware queues on the NIC for automatic packet sorting. Keeps the vSwitch active. Best for general virtualization with live migration.
Notes: Good morning, everyone. Today, we're diving deep into the critical world of network I/O virtualization, a topic central to high-performance data centers and NFV deployments. We'll be dissecting three key technologies: DPDK, SR-IOV, and VMDq. These aren't just buzzwords; they represent fundamental shifts in how we handle network traffic in virtualized environments. Each offers a distinct approach to overcoming the inherent bottlenecks of traditional networking. We'll explore their architectures, their trade-offs, and ultimately, how to choose the right tool for the right job. Let's start by understanding the core problem these technologies aim to solve.

## Slide 2
BACKGROUND
Server Virtualization
Network I/O Virtualization Technologies
Originally, host servers were configured with one network connection per VM.
As 10GbE NICs started to enter the market, it became more cost effective to share a single connection among multiple VMs.
vSwitch to a virtual top of rack (ToR) switch within the hypervisor, while the NIC provides the uplink ports for this virtual ToR that are shared among multiple servers.
Notes: The fundamental challenge we face in modern data centers is that traditional kernel networking simply cannot keep pace with the demands of high-speed virtualized environments. When we're pushing 10 gigabits per second and beyond, the overhead of the standard packet path becomes a severe bottleneck. Every single packet triggers a CPU interrupt, forcing the CPU to context switch and process it through the kernel's network stack. This isn't just about CPU cycles; it's about multiple memory copies and the software virtual switch having to inspect and sort every frame. At high packet rates, say over a million packets per second, this overhead doesn't just add latency; it consumes entire CPU cores, leading to a non-linear degradation in performance. We need a better way to move packets efficiently. So, let's look at how the industry has responded to this challenge.

## Slide 3
BACKGROUND
Traditional Kernel Networking Cannot Keep Pace with Modern Data Center Demands
In a standard virtualized environment, every incoming network packet must travel through the host OS kernel before reaching a virtual machine. At 10 Gbps and above, this overhead consumes entire CPU cores and introduces microseconds of latency per packet — creating a severe bottleneck that limits both throughput and application density.
01
CPU Interrupt Per Packet
Every arriving packet fires a hardware interrupt (IRQ), forcing the CPU to stop its current task, save state, and invoke the kernel NIC driver — consuming cycles on every single frame.
02
Multiple Memory Copies
Packet data is copied at least twice: from NIC DMA to host kernel memory, then from host memory to VM guest memory — each copy consuming CPU cycles and memory bandwidth.
Network I/O Virtualization Technologies
03
Software vSwitch Sorting Overhead
The hypervisor's software vSwitch must inspect the destination MAC and VLAN of every frame and sort it to the correct VM — a CPU-intensive operation that scales linearly with packet rate.
04
Context Switches Between Kernel and Hypervisor
Each packet traversal involves multiple privilege-level transitions between user space, kernel space, and the hypervisor VMM — each transition flushing CPU pipeline state.
05
Non-Linear Degradation at Scale
Performance degrades severely above 1 million packets per second (Mpps). At 10 Gbps with 64-byte frames, the system must process ~14.8 Mpps — far beyond what the kernel path can sustain.
02 / 15
Notes: The fundamental challenge we face in modern data centers is that traditional kernel networking simply cannot keep pace with the demands of high-speed virtualized environments. When we're pushing 10 gigabits per second and beyond, the overhead of the standard packet path becomes a severe bottleneck. Every single packet triggers a CPU interrupt, forcing the CPU to context switch and process it through the kernel's network stack. This isn't just about CPU cycles; it's about multiple memory copies and the software virtual switch having to inspect and sort every frame. At high packet rates, say over a million packets per second, this overhead doesn't just add latency; it consumes entire CPU cores, leading to a non-linear degradation in performance. We need a better way to move packets efficiently. So, let's look at how the industry has responded to this challenge.

## Slide 4
BACKGROUND
Virtual Machines Device Queues (VMDq)
Network I/O Virtualization Technologies
Within the network interface controller (NIC), both transmit and receive queues are established for each VM hosted in the server..
When frames are received from the physical network, MAC address and VLAN tag information in the frame headers can be used to determine the correct VM to send the traffic to.
Notes: The fundamental challenge we face in modern data centers is that traditional kernel networking simply cannot keep pace with the demands of high-speed virtualized environments. When we're pushing 10 gigabits per second and beyond, the overhead of the standard packet path becomes a severe bottleneck. Every single packet triggers a CPU interrupt, forcing the CPU to context switch and process it through the kernel's network stack. This isn't just about CPU cycles; it's about multiple memory copies and the software virtual switch having to inspect and sort every frame. At high packet rates, say over a million packets per second, this overhead doesn't just add latency; it consumes entire CPU cores, leading to a non-linear degradation in performance. We need a better way to move packets efficiently. So, let's look at how the industry has responded to this challenge.

## Slide 5
BACKGROUND
Virtual Machines Device Queues (VMDq)
Network I/O Virtualization Technologies
The vSwitch simply needs to forward the frame to the VM from the corresponding queue. When packets are transmitted from the VM, they are simply forwarded to the associated queue in the NIC.
The NIC can then send frames out to the physical network based on various scheduling mechanisms such as round robin, weighted round robin, or strict priority based on service level agreements.
Notes: The fundamental challenge we face in modern data centers is that traditional kernel networking simply cannot keep pace with the demands of high-speed virtualized environments. When we're pushing 10 gigabits per second and beyond, the overhead of the standard packet path becomes a severe bottleneck. Every single packet triggers a CPU interrupt, forcing the CPU to context switch and process it through the kernel's network stack. This isn't just about CPU cycles; it's about multiple memory copies and the software virtual switch having to inspect and sort every frame. At high packet rates, say over a million packets per second, this overhead doesn't just add latency; it consumes entire CPU cores, leading to a non-linear degradation in performance. We need a better way to move packets efficiently. So, let's look at how the industry has responded to this challenge.

## Slide 6
VMDQ ARCHITECTURE
VMDQ · HYPERVISOR OFFLOAD · INTEL HARDWARE
Intelligent Hardware Queue Offload Reduces Hypervisor CPU Without Removing the vSwitch
VMDq assigns each VM a dedicated hardware RX queue on the NIC. The NIC hardware classifies every incoming frame by its destination MAC address and VLAN ID, placing it directly into the correct VM's queue. The hypervisor vSwitch then picks up pre-sorted packets and delivers them — its most expensive operation, per-packet sorting, has been eliminated in silicon. The vSwitch remains fully in the data path, preserving live migration, security groups, and traffic monitoring.
ARCHITECTURE COMPARISON — NORMAL VS VMDQ VS SR-IOV
ARCHITECTURE SUMMARY
Per-VM Hardware RX Queues
Each VM is assigned a dedicated hardware queue on the NIC. No shared queue contention between VMs.
NIC Classifies by MAC + VLAN
The NIC hardware inspects destination MAC address and VLAN tag and routes each frame to the matching VM queue — no CPU involvement in sorting.
Hypervisor vSwitch Completes Delivery
The vSwitch remains active for final delivery and all policy enforcement — ACLs, QoS, port mirroring, and security groups all function normally.
Full Live Migration Support
Because no hardware VF is directly bound to the VM, the hypervisor can migrate VMs between hosts without network interruption.
Network I/O Virtualization Technologies
Notes: VMDq, or Virtual Machine Device Queues, is an Intel hardware-assist technology designed to alleviate one of the most CPU-intensive tasks of the software virtual switch: packet sorting. Instead of the hypervisor's CPU having to inspect every incoming packet to determine its destination VM, VMDq offloads this classification to the NIC hardware. Each VM gets its own dedicated hardware receive queue. The NIC then intelligently classifies incoming frames based on their MAC address and VLAN ID, placing them directly into the correct VM's queue. This means the hypervisor's vSwitch still handles final delivery and policy enforcement, but its most expensive operation has been moved into silicon. This approach maintains full compatibility with features like live migration, which is a significant advantage in many enterprise environments. Now, let's weigh the pros and cons of this approach.

## Slide 7
VMDQ ARCHITECTURE
VMDQ · HYPERVISOR OFFLOAD · INTEL HARDWARE
Intelligent Hardware Queue Offload Reduces Hypervisor CPU Without Removing the vSwitch
ARCHITECTURE COMPARISON — NORMAL VS VMDQ VS SR-IOV
BEST SUITED FOR
General-purpose enterprise virtualization (VMware vSphere, Hyper-V, KVM) where live migration is required and a moderate performance improvement over standard virtio is desired without the hardware constraints.
08 / 15
Notes: VMDq, or Virtual Machine Device Queues, is an Intel hardware-assist technology designed to alleviate one of the most CPU-intensive tasks of the software virtual switch: packet sorting. Instead of the hypervisor's CPU having to inspect every incoming packet to determine its destination VM, VMDq offloads this classification to the NIC hardware. Each VM gets its own dedicated hardware receive queue. The NIC then intelligently classifies incoming frames based on their MAC address and VLAN ID, placing them directly into the correct VM's queue. This means the hypervisor's vSwitch still handles final delivery and policy enforcement, but its most expensive operation has been moved into silicon. This approach maintains full compatibility with features like live migration, which is a significant advantage in many enterprise environments. Now, let's weigh the pros and cons of this approach.

## Slide 8
VMDQ ARCHITECTURE
VMDQ · HYPERVISOR OFFLOAD · INTEL HARDWARE
Intelligent Hardware Queue Offload Reduces Hypervisor CPU Without Removing the vSwitch
ARCHITECTURE COMPARISON — NORMAL VS VMDQ VS SR-IOV
YouTube
Intel VMDq Explanation
https://www.youtube.com/watch?v=QvKXbpV6WXk
08 / 15
Notes: VMDq, or Virtual Machine Device Queues, is an Intel hardware-assist technology designed to alleviate one of the most CPU-intensive tasks of the software virtual switch: packet sorting. Instead of the hypervisor's CPU having to inspect every incoming packet to determine its destination VM, VMDq offloads this classification to the NIC hardware. Each VM gets its own dedicated hardware receive queue. The NIC then intelligently classifies incoming frames based on their MAC address and VLAN ID, placing them directly into the correct VM's queue. This means the hypervisor's vSwitch still handles final delivery and policy enforcement, but its most expensive operation has been moved into silicon. This approach maintains full compatibility with features like live migration, which is a significant advantage in many enterprise environments. Now, let's weigh the pros and cons of this approach.

## Slide 9
VMDQ — VIRTUAL MACHINE DEVICE QUEUES
VMDq Offers a Practical Performance Boost with Full Hypervisor Compatibility, but Cannot Match SR-IOV Throughput
VMDQ
Advantages
+
Reduces Hypervisor CPU Load for Packet Sorting
By offloading per-packet MAC and VLAN classification to NIC hardware, VMDq frees the hypervisor CPU from its most expensive per-packet task, allowing those cycles to serve other VM workloads instead.
+
Full VM Live Migration Support
Because no hardware VF is directly bound to the VM, the hypervisor can migrate VMs between physical hosts without any network interruption — a critical operational requirement in enterprise environments.
+
Retains All vSwitch Features
Security groups, ACLs, port mirroring, QoS policies, and traffic monitoring all continue to function normally because the hypervisor vSwitch remains fully in the data path for final delivery and policy enforcement.
+
Simpler to Deploy than SR-IOV
VMDq requires no BIOS changes, no IOMMU configuration, and no per-VM hardware assignment. It integrates transparently with VMware vSphere (NetQueue), Microsoft Hyper-V (VMQ), and KVM with compatible Intel NICs.
Disadvantages
−
Lower Peak Performance than SR-IOV or DPDK
VMDq does not eliminate the hypervisor from the data path — it only removes the sorting step. The vSwitch still processes every packet and the hypervisor still performs the memory copy from host to VM memory, capping peak throughput well below SR-IOV levels.
−
Intel-Proprietary Technology
VMDq is not an open standard — it is an Intel-specific feature available only on Intel-branded NIC hardware. This limits hardware vendor choice and creates a dependency on Intel's product roadmap and driver support.
−
Mutually Exclusive with SR-IOV on the Same Port
A NIC port can operate in either SR-IOV mode (exposing VFs) or VMDq mode (exposing hardware queues to the hypervisor), but not both simultaneously. Choosing VMDq means forgoing SR-IOV for that port's traffic.
−
Limited Number of Hardware Queues
The number of VMDq hardware queues is finite and NIC-model dependent — typically 64 to 128 queues. In dense VM environments, queues must be shared, reducing the sorting benefit and potentially reintroducing software classification overhead.
KEY INSIGHT
VMDq occupies the middle ground between standard software switching and full SR-IOV bypass. It is the right choice when live migration is non-negotiable and a moderate throughput improvement is sufficient — but for maximum performance, SR-IOV or DPDK should be preferred.
Network I/O Virtualization Technologies
09 / 15
Notes: VMDq offers a practical and often sufficient performance boost, especially in general-purpose enterprise virtualization. Its primary advantage is significantly reducing the hypervisor's CPU load for packet sorting, freeing up those cycles for other VM workloads. Crucially, it maintains full compatibility with essential hypervisor features like live migration, security groups, and QoS policies, because the vSwitch remains in the data path. Deployment is also simpler than SR-IOV, requiring no complex BIOS or IOMMU configurations. However, VMDq doesn't eliminate the hypervisor from the data path entirely; it only offloads the sorting. This means its peak performance won't match SR-IOV or DPDK. It's also an Intel-proprietary technology, limiting hardware choice, and it's mutually exclusive with SR-IOV on the same port. So, VMDq is a great middle-ground solution when live migration is paramount and a moderate performance gain is acceptable. Next, we'll explore SR-IOV, which takes a much more aggressive approach to performance.

## Slide 10
VMDQ ARCHITECTURE
VMDQ · HYPERVISOR OFFLOAD · INTEL HARDWARE
Intelligent Hardware Queue Offload Reduces Hypervisor CPU Without Removing the vSwitch
ARCHITECTURE COMPARISON — NORMAL VS VMDQ VS SR-IOV
YouTube
Intel SR-IOV Explanation
https://www.youtube.com/watch?v=hRHsk8Nycdg&t=85s
08 / 15
Notes: VMDq, or Virtual Machine Device Queues, is an Intel hardware-assist technology designed to alleviate one of the most CPU-intensive tasks of the software virtual switch: packet sorting. Instead of the hypervisor's CPU having to inspect every incoming packet to determine its destination VM, VMDq offloads this classification to the NIC hardware. Each VM gets its own dedicated hardware receive queue. The NIC then intelligently classifies incoming frames based on their MAC address and VLAN ID, placing them directly into the correct VM's queue. This means the hypervisor's vSwitch still handles final delivery and policy enforcement, but its most expensive operation has been moved into silicon. This approach maintains full compatibility with features like live migration, which is a significant advantage in many enterprise environments. Now, let's weigh the pros and cons of this approach.

## Slide 11
VMDQ — VIRTUAL MACHINE DEVICE QUEUES
VMDq Offers a Practical Performance Boost with Full Hypervisor Compatibility, but Cannot Match SR-IOV Throughput
VMDQ
Advantages
+
Reduces Hypervisor CPU Load for Packet Sorting
By offloading per-packet MAC and VLAN classification to NIC hardware, VMDq frees the hypervisor CPU from its most expensive per-packet task, allowing those cycles to serve other VM workloads instead.
+
Full VM Live Migration Support
Because no hardware VF is directly bound to the VM, the hypervisor can migrate VMs between physical hosts without any network interruption — a critical operational requirement in enterprise environments.
+
Retains All vSwitch Features
Security groups, ACLs, port mirroring, QoS policies, and traffic monitoring all continue to function normally because the hypervisor vSwitch remains fully in the data path for final delivery and policy enforcement.
+
Simpler to Deploy than SR-IOV
VMDq requires no BIOS changes, no IOMMU configuration, and no per-VM hardware assignment. It integrates transparently with VMware vSphere (NetQueue), Microsoft Hyper-V (VMQ), and KVM with compatible Intel NICs.
Disadvantages
−
Lower Peak Performance than SR-IOV or DPDK
VMDq does not eliminate the hypervisor from the data path — it only removes the sorting step. The vSwitch still processes every packet and the hypervisor still performs the memory copy from host to VM memory, capping peak throughput well below SR-IOV levels.
−
Intel-Proprietary Technology
VMDq is not an open standard — it is an Intel-specific feature available only on Intel-branded NIC hardware. This limits hardware vendor choice and creates a dependency on Intel's product roadmap and driver support.
−
Mutually Exclusive with SR-IOV on the Same Port
A NIC port can operate in either SR-IOV mode (exposing VFs) or VMDq mode (exposing hardware queues to the hypervisor), but not both simultaneously. Choosing VMDq means forgoing SR-IOV for that port's traffic.
−
Limited Number of Hardware Queues
The number of VMDq hardware queues is finite and NIC-model dependent — typically 64 to 128 queues. In dense VM environments, queues must be shared, reducing the sorting benefit and potentially reintroducing software classification overhead.
KEY INSIGHT
VMDq occupies the middle ground between standard software switching and full SR-IOV bypass. It is the right choice when live migration is non-negotiable and a moderate throughput improvement is sufficient — but for maximum performance, SR-IOV or DPDK should be preferred.
Network I/O Virtualization Technologies
09 / 15
Notes: VMDq offers a practical and often sufficient performance boost, especially in general-purpose enterprise virtualization. Its primary advantage is significantly reducing the hypervisor's CPU load for packet sorting, freeing up those cycles for other VM workloads. Crucially, it maintains full compatibility with essential hypervisor features like live migration, security groups, and QoS policies, because the vSwitch remains in the data path. Deployment is also simpler than SR-IOV, requiring no complex BIOS or IOMMU configurations. However, VMDq doesn't eliminate the hypervisor from the data path entirely; it only offloads the sorting. This means its peak performance won't match SR-IOV or DPDK. It's also an Intel-proprietary technology, limiting hardware choice, and it's mutually exclusive with SR-IOV on the same port. So, VMDq is a great middle-ground solution when live migration is paramount and a moderate performance gain is acceptable. Next, we'll explore SR-IOV, which takes a much more aggressive approach to performance.

## Slide 12
SR-IOV ARCHITECTURE
Hardware Bypass via PCIe Virtualization: SR-IOV
SR-IOV is a PCI-SIG standard that allows a single physical NIC to present itself as multiple independent PCIe devices. The NIC exposes one Physical Function (PF) controlled by the hypervisor, and up to 256 Virtual Functions (VFs) — lightweight hardware endpoints passed directly into VMs. Each VF has its own dedicated TX/RX descriptor rings, interrupt vectors, and DMA channels. When a VM is assigned a VF, it communicates directly with the NIC hardware using Intel VT-d or AMD-Vi IOMMU for DMA address translation, completely bypassing the hypervisor's virtual switch and VMM data path.
SR-IOV PACKET PATH (RX)
Physical NIC + eSwitch
→
VF DMA Ring
→
Hypervisor vSwitch
→
IOMMU / VT-d
→
VM Guest Memory
⊘ Hypervisor vSwitch and VMM are completely bypassed
ARCHITECTURE COMPONENTS
PF
Physical Function — Hypervisor Control Plane
The PF is the full-featured PCIe function owned by the hypervisor's host driver. It configures the NIC eSwitch forwarding rules, creates and destroys VFs, assigns MAC addresses and VLAN IDs to each VF, and manages SR-IOV global state. The PF is never in the data path for VM traffic.
VF
Virtual Function — VM Data Plane
Each VF is a lightweight PCIe endpoint assigned directly to a VM via PCIe passthrough. It has its own TX/RX descriptor rings, MSI-X interrupt vectors, and a dedicated DMA channel. The VM's guest driver communicates with the VF as if it were a physical NIC, with no hypervisor involvement in the data path.
ESWITCH
NIC Embedded Switch — Hardware L2 Forwarding
The eSwitch is a hardware Layer 2 switch implemented in NIC silicon. It maintains a forwarding table of MAC address and VLAN ID entries, each mapped to a specific VF's VPort. Inbound frames are classified and forwarded to the correct VF entirely in hardware — no CPU involvement, no software lookup.
IOMMU
IOMMU / VT-d — Safe DMA Address Translation
The IOMMU (Intel VT-d or AMD-Vi) translates the VM's physical I/O addresses to actual host physical memory addresses, allowing the VF to DMA packet data directly into VM guest memory without CPU involvement. This provides memory isolation between VMs, preventing one VM from accessing another's memory via DMA.
Network I/O Virtualization Technologies
06 / 15
Notes: SR-IOV offers a powerful way to achieve near bare-metal network performance within a virtualized environment. It does this by allowing a physical NIC to present itself as multiple independent PCIe devices. The key here is that a Virtual Function, or VF, is passed directly to a VM, completely bypassing the hypervisor's virtual switch and VMM data path. This direct access means the VM communicates with the NIC hardware as if it were a physical device, leveraging the IOMMU for secure DMA address translation. This architecture effectively removes several layers of software overhead, which we saw were bottlenecks in traditional networking. Now, let's look at the specific advantages and disadvantages of this approach.

## Slide 13
SR-IOV — SINGLE ROOT I/O VIRTUALIZATION
SR-IOV Achieves the Highest Possible Performance but Sacrifices VM Mobility and Traffic Visibility
Advantages
+
Near Bare-Metal Network Performance
SR-IOV delivers throughput within 1–3% of native NIC performance. The host CPU is almost entirely removed from the data path — no interrupts, no memory copies, no vSwitch processing per packet.
+
Very Low Host CPU Overhead
Because the NIC's eSwitch handles all frame forwarding in hardware and IOMMU DMA delivers packets directly to VM memory, the host CPU is not involved in the data path at all — freeing cores for other workloads.
+
Open PCI-SIG Standard
SR-IOV is a ratified PCI-SIG standard supported by all major NIC vendors — Intel, Mellanox/NVIDIA, Broadcom, and Chelsio — ensuring broad hardware compatibility and long-term vendor support.
+
Ideal for Latency-Sensitive Workloads
Single-digit microsecond latency makes SR-IOV the preferred choice for telecom NFV (vRouter, vFirewall, 5G UPF), high-frequency trading, and HPC interconnect applications.
Disadvantages
−
Strict Hardware Requirements
Requires a NIC, motherboard, and BIOS that all explicitly support SR-IOV, plus IOMMU (Intel VT-d or AMD-Vi) enabled in the BIOS. Not all commodity server hardware meets these requirements.
−
VM Live Migration is Difficult or Restricted
A VM holding a VF has a direct hardware reference to a specific physical NIC. Moving the VM to another host requires detaching and reattaching the VF, causing a brief network interruption — incompatible with seamless live migration.
−
No vSwitch Features on SR-IOV Paths
Security groups, ACLs, port mirroring, QoS policies, and traffic monitoring are all unavailable for SR-IOV traffic paths, as there is no software switch in the path to enforce them.
−
VM-to-VM Traffic on Same Host Requires External Switch
Without switchdev or hairpin mode, East-West traffic between two SR-IOV VMs on the same host must leave the server, traverse the physical switch, and return — adding latency and consuming uplink bandwidth.
KEY INSIGHT
SR-IOV is the right choice when North-South throughput and latency are the primary concern and VM live migration is not a hard operational requirement. Combining SR-IOV with DPDK inside the VM eliminates both the hypervisor and guest kernel overhead simultaneously.
Network I/O Virtualization Technologies
07 / 15
Notes: SR-IOV delivers the closest performance to bare metal of any virtualization networking technology, often within 1 to 3% of native NIC throughput. The host CPU is almost entirely removed from the data path, freeing up valuable cycles for other workloads. This makes SR-IOV ideal for latency-sensitive applications like high-frequency trading or telecom NFV. However, this performance comes with trade-offs. SR-IOV has strict hardware requirements, needing specific NIC, motherboard, and BIOS support. More critically, VM live migration is severely restricted because the VM holds a direct hardware reference to a specific physical NIC's VF. This means features like security groups and traffic monitoring are unavailable for SR-IOV paths. So, while it offers incredible speed, it sacrifices some operational flexibility. Next, we'll shift our focus to DPDK, a software-based approach to kernel bypass.

## Slide 14
Data Plane Development Kit (DPDK)
The Data Plane Development Kit (DPDK) is an open-source software project managed by the Linux Foundation
It provides a set of data plane libraries and network interface controller polling-mode drivers for offloading packet processing from the operating system kernel to processes running in user space.
This offloading achieves higher computing efficiency and higher packet throughput than is possible using the interrupt-driven processing provided in the kernel.
DPDK provides a programming framework for x86, ARM, and PowerPC processors and enables faster development of high-speed data packet networking applications.
Data Plane Development Kit (DPDK)

## Slide 15
Data Plane Development Kit (DPDK)
In order to understand DPDK , we should know how Linux handles the networking part.
By default Linux uses kernel to process packets, this puts pressure on kernel to process packets faster as the NICs (Network Interface Card) speeds are increasing at fast.
There have been many techniques to bypass kernel to achieve packet efficiency.
This involves processing packets in the userspace instead of kernel space.
DPDK is one such technology.
Data Plane Development Kit (DPDK)

## Slide 16
Data Plane Development Kit (DPDK)
User space versus kernel space in Linux?
Kernel space is where the kernel (i.e., the core of the operating system) runs and provides its services. It sets things up so separate user processes see and manipulate only their own memory space.
User space is that portion of system memory in which user processes run . Kernel space can be accessed by user processes only through the use of system calls.
Data Plane Development Kit (DPDK)

## Slide 17: Data Plane Development Kit (DPDK)

## Slide 18
Data Plane Development Kit (DPDK)
Without DPDK, packet processing is through the kernel network stack which is interrupt-driven.
Each time NIC receives incoming packets, there is a kernel interrupt to process the packets and a context switch from kernel space to user space.
This creates delay.
Data Plane Development Kit (DPDK)

## Slide 19
Data Plane Development Kit (DPDK)
With the DPDK, there is no need for interrupts, as the processing happens in user space using Poll mode drivers.
These poll mode drivers can poll data directly from NIC, thus provide fast switching by completely bypassing kernel space. This improves the throughput rate of data.
Now after we know the basics of how Linux networking stack works and what is the role of DPDK, we turn our attention on how OVS (Open vSwitch ) works with and without DPDK.
Data Plane Development Kit (DPDK)

## Slide 20
Data Plane Development Kit (DPDK) with OVS
What is OVS (Open vSwitch)? Open vSwitch is a production quality, multilayer virtual switch licensed under the open source Apache 2.0.
This runs as software in hypervisor and enables virtual networking of Virtual Machines.
Main components include:
  Forwarding path: Datapath/Forwarding path is the main packet forwarding module of OVS, implemented in kernel space for high performance/
  Vswitchid is the main Open vSwitch userspace program.

## Slide 21
DPDK — ARCHITECTURE
DPDK Delivers Near-Line-Rate Performance by Eliminating the OS Kernel from the Packet Path
DPDK PACKET PATH (RX)
DPDK Application
User Space · VM / Container
Poll Mode Driver (PMD)
User Space · Spins on RX/TX rings
Kernel vSwitch / OVS
Bypassed — no kernel context switch
BYPASSED
Kernel TCP/IP Stack
Bypassed — no socket buffer
BYPASSED
Kernel NIC Driver
Bypassed — no IRQ handler
BYPASSED
DMA Engine
Hugepages · No CPU copy
Physical NIC
rte_flow · RSS · MAC/VLAN steering
Poll Mode Driver (PMD)
Instead of waiting for hardware interrupts, a dedicated CPU core runs in a tight polling loop, continuously checking the NIC's RX descriptor ring for new packets. This eliminates interrupt latency, IRQ handler overhead, and all kernel context switching — at the cost of that core being fully occupied even when the NIC is idle.
Hugepages and Zero-Copy Memory
DPDK allocates large memory pages (2 MB or 1 GB hugepages) for its packet buffer pools (mempools). This dramatically reduces TLB miss rates and allows the NIC to DMA packet data directly into user-space memory without any kernel involvement or additional memory copies — achieving true zero-copy packet handling.
rte_flow and Receive-Side Scaling (RSS)
The rte_flow API programs the NIC hardware to steer specific traffic flows directly to designated CPU core queues based on L2–L4 header fields. RSS distributes packets across multiple cores by hashing the 5-tuple (src/dst IP, src/dst port, protocol), enabling linear throughput scaling across many CPU cores without software load balancing.
Best Use Cases
DPDK excels for East-West traffic (VM-to-VM on the same host), NFV service chaining (vRouter → vFirewall → vLB pipelines), and high-performance virtual switching via OVS-DPDK or VPP. It is the preferred data-plane framework for 5G UPF, virtual DPI, and any application requiring programmable packet processing at line rate.
KEY FACTS
Open Source — Linux Foundation
Works on Standard NICs
No Special Hardware Required
Typical Throughput: 10–100 Gbps / core
Network I/O Virtualization Technologies
04 / 15
Notes: DPDK, or the Data Plane Development Kit, is an open-source software framework that achieves near-line-rate performance by completely eliminating the OS kernel from the packet path. Instead of relying on interrupts, DPDK dedicates CPU cores to continuously poll the NIC for incoming packets. This polling model, while consuming dedicated CPU resources, eliminates interrupt overhead, context switching, and kernel system call latency. Packets are received directly into user-space memory buffers using hugepages, processed by the application, and transmitted back to the NIC without any kernel involvement. This makes DPDK particularly well-suited for East-West traffic, NFV service chaining, and high-performance virtual switching. Now, let's examine the specific advantages and disadvantages of this software-centric approach.

## Slide 22
DPDK — EVALUATION
DPDK Offers Unmatched Flexibility but Demands Dedicated CPU Resources and Engineering Effort
DPDK
Advantages
Extremely High Throughput and Low Latency
Commonly achieves 10–100 Gbps on a single core with sub-microsecond latency, by eliminating all kernel overhead from the packet path.
No Special Hardware Required
Works on standard commodity NICs from Intel, Mellanox, Broadcom, and others. No BIOS changes, IOMMU configuration, or SR-IOV capable hardware needed.
Highly Flexible and Programmable
Developers can implement custom packet processing pipelines, load balancers, firewalls, and virtual switches entirely in user space using the full DPDK API.
Foundation for OVS-DPDK and VPP
Integrates naturally with Open vSwitch (OVS-DPDK) for high-performance East-West VM-to-VM switching and is the basis of the Vector Packet Processing (VPP) framework.
Disadvantages
Dedicated CPU Cores Consumed by Busy-Polling
The polling model permanently occupies dedicated CPU cores even when no traffic is present — those cores cannot be shared with or reclaimed by other workloads.
Standard Linux Tools Do Not Work
tcpdump, iptables, netstat, and other standard Linux network utilities cannot observe or interact with DPDK-managed interfaces, complicating troubleshooting and monitoring.
High Development Complexity
Requires expertise in lock-free data structures, NUMA-aware memory allocation, hugepage management, and NIC-specific PMD behaviour — significantly steeper than standard socket programming.
Live Migration Requires Additional Configuration
VM live migration is only possible when combined with OVS-DPDK, which adds considerable configuration and operational complexity compared to standard virtio networking.
Combined Usage: SR-IOV + DPDK is the premier NFV combination — SR-IOV bypasses the hypervisor vSwitch, then DPDK bypasses the guest kernel, creating a two-level bypass that delivers near bare-metal performance inside a VM.
Network I/O Virtualization Technologies
05 / 15
Notes: DPDK offers unmatched flexibility and extremely high throughput, often achieving 10 to 100 gigabits per second on a single core with sub-microsecond latency. It requires no special NIC hardware, running on standard commodity adapters, and is highly programmable, allowing developers to build custom packet processing pipelines. This makes it a cornerstone for projects like OVS-DPDK and VPP. However, this power comes with its own set of challenges. The polling model permanently occupies dedicated CPU cores, even when there's no traffic, which means those cores can't be used for other workloads. Standard Linux network tools also don't work on DPDK interfaces, complicating troubleshooting. Development complexity is significantly higher, requiring specialized expertise. Live VM migration is also more complex, typically requiring OVS-DPDK. So, while DPDK delivers incredible performance and flexibility, it demands dedicated resources and a higher engineering effort. We've discussed how SR-IOV and DPDK bypass different layers of the networking stack. But what happens to the concept of switching when these technologies are in play?

## Slide 23
VMDQ ARCHITECTURE
VMDQ · HYPERVISOR OFFLOAD · INTEL HARDWARE
Intelligent Hardware Queue Offload Reduces Hypervisor CPU Without Removing the vSwitch
ARCHITECTURE COMPARISON — NORMAL VS VMDQ VS SR-IOV
YouTube
Intel DPDK Explanation
https://www.youtube.com/watch?v=1DWxo2gF-RQ&t=320s
08 / 15
Notes: VMDq, or Virtual Machine Device Queues, is an Intel hardware-assist technology designed to alleviate one of the most CPU-intensive tasks of the software virtual switch: packet sorting. Instead of the hypervisor's CPU having to inspect every incoming packet to determine its destination VM, VMDq offloads this classification to the NIC hardware. Each VM gets its own dedicated hardware receive queue. The NIC then intelligently classifies incoming frames based on their MAC address and VLAN ID, placing them directly into the correct VM's queue. This means the hypervisor's vSwitch still handles final delivery and policy enforcement, but its most expensive operation has been moved into silicon. This approach maintains full compatibility with features like live migration, which is a significant advantage in many enterprise environments. Now, let's weigh the pros and cons of this approach.

## Slide 24
ADDRESSING AND FORWARDING — CROSS-TECHNOLOGY ANALYSIS
Switching Is Never Eliminated — It Moves Into Silicon, User Space, or the NIC Queue
All three technologies bypass the software virtual switch, but switching still occurs using MAC address and VLAN tag addressing. The function is relocated to hardware, user space, or pre-sorted NIC queues rather than in the kernel.
SR-IOV
NIC HARDWARE ESWITCH
WHERE SWITCHING HAPPENS
Inside the NIC Silicon
The NIC contains a hardware eSwitch that maps MAC+VLAN to VF ports in silicon.
ADDRESSING MECHANISM
MAC Address + VLAN ID per VF
The PF assigns each VF a MAC and optional VLAN; the eSwitch classifies frames and delivers them to the correct VF without CPU involvement.
VM-TO-VM ON SAME HOST
Requires External Switch or switchdev
East–West traffic leaves the server unless the eSwitch is programmed for local forwarding (switchdev/hairpin).
DPDK
USER-SPACE FLOW TABLE
WHERE SWITCHING HAPPENS
User Space (OVS-DPDK or rte_flow)
DPDK runs switching in user space or offloads rules to NIC hardware (rte_flow).
ADDRESSING MECHANISM
L2–L4 Header Matching + RSS Hashing
Packets are classified by headers; RSS hashes flows across CPU cores for parallel processing.
VM-TO-VM ON SAME HOST
Handled Entirely in User Space
OVS-DPDK forwards intra-host VM traffic in user space with no kernel crossing.
VMDq
NIC PRE-SORT + VSWITCH DELIVERY
WHERE SWITCHING HAPPENS
vSwitch Still Makes Final Decision
VMDq pre-sorts packets but the hypervisor vSwitch performs the final forwarding decision.
ADDRESSING MECHANISM
MAC + VLAN for Queue Assignment
The NIC assigns packets to per-VM queues by MAC and VLAN; the vSwitch reads the right queue.
VM-TO-VM ON SAME HOST
Handled by the Hypervisor vSwitch
Intra-host forwarding is still done by the vSwitch; VMDq mainly improves ingress classification.
COMMON THREAD
MAC addresses and VLAN tags are the universal addressing mechanism. The difference is where the lookup table lives — NIC eSwitch (SR-IOV), user-space flow table (DPDK), or NIC pre-sort queues with vSwitch delivery (VMDq).
Network I/O Virtualization Technologies
10 / 15
Notes: A common misconception is that SR-IOV and DPDK eliminate switching entirely. In reality, switching is never truly eliminated; it's simply moved to a different location within the architecture. For SR-IOV, the NIC itself contains an embedded switch, or eSwitch, which performs hardware-based Layer 2 forwarding. The hypervisor programs this eSwitch, and then the NIC handles packet delivery to the correct Virtual Function in hardware, without CPU involvement. With DPDK, especially in an OVS-DPDK setup, the switching table lives in user-space memory, and the Poll Mode Driver consults it at line rate, replacing the kernel vSwitch with a faster software equivalent. VMDq, as we discussed, uses NIC hardware to pre-sort frames, but the final forwarding decision still rests with the hypervisor's vSwitch. The common thread across all these approaches is the reliance on MAC addresses and VLAN tags for addressing. The key difference is where that lookup and forwarding decision happens. Next, we'll explore how SR-IOV and DPDK can be combined for even greater performance.

## Slide 25
OVERVIEW
Three Solutions, Each Targeting a Different Layer of Overhead
DPDK
Data Plane Development Kit
KERNEL BYPASS · SOFTWARE
DPDK is an open-source framework of libraries and Poll Mode Drivers (PMDs) that moves all packet processing out of the OS kernel into user space. Dedicated CPU cores run in a continuous polling loop, eliminating hardware interrupts and context switching entirely. Packets are handled directly in user-space memory using hugepages, with no kernel system calls in the data path.
LAYER BYPASSED
OS Kernel + Interrupt Model
SR-IOV
Single Root I/O Virtualization
HARDWARE BYPASS · PCIE STANDARD
SR-IOV is a PCI-SIG hardware standard that partitions a single physical NIC into a Physical Function (PF) and multiple Virtual Functions (VFs). Each VF is a lightweight hardware endpoint assigned directly to a VM. Traffic flows via IOMMU-protected DMA directly between the NIC and VM guest memory, completely bypassing the hypervisor's virtual switch and VMM data path.
LAYER BYPASSED
Hypervisor vSwitch + VMM
VMDq
Virtual Machine Device Queues
HYPERVISOR OFFLOAD · INTEL HW
VMDq is an Intel hardware-assist technology that offloads the most CPU-intensive task of the software vSwitch — per-packet sorting — into dedicated NIC hardware queues. Each VM is assigned its own hardware RX queue, and the NIC automatically classifies incoming frames by MAC address and VLAN ID. The hypervisor vSwitch remains in the path but is relieved of its sorting burden.
LAYER OFFLOADED
Hypervisor CPU Sorting Cost
BYPASS POINTS
DPDK Removes kernel stack & interrupt model
SR-IOV Removes hypervisor vSwitch & VMM
VMDq Removes CPU sorting overhead only
Network I/O Virtualization Technologies
03 / 15
Notes: To address these bottlenecks, the industry hasn't settled on a single solution, but rather three distinct approaches: DPDK, SR-IOV, and VMDq. Each of these technologies targets a different layer of overhead in that traditional packet path we just discussed. DPDK, for instance, is a software framework that completely bypasses the kernel, moving packet processing into user space. SR-IOV, on the other hand, is a hardware standard that allows virtual machines direct access to the NIC, effectively bypassing the hypervisor's virtual switch. And then we have VMDq, an Intel hardware offload that intelligently sorts packets on the NIC itself, reducing the CPU burden on the hypervisor. Understanding where each technology intervenes is crucial for selecting the optimal solution for your specific workload. Let's dive into the details of VMDq first.

## Slide 26
COMPARISON
Side-by-Side: Standard Virtualization vs DPDK vs SR-IOV vs VMDq
Standard
DPDK
SR-IOV
VMDq
CRITERIA
Standard
Software vSwitch
DPDK
Kernel-Bypass (SW)
SR-IOV
Hardware VF Bypass
VMDq
HW Queue Offload
METHOD
Software vSwitch in kernel; all packets processed by host OS
User-space Poll Mode Driver; kernel completely bypassed
PCIe Virtual Functions; VM talks directly to NIC hardware
NIC sorts packets into per-VM HW queues; vSwitch delivers
VSWITCH ROLE
Full involvement
— sorts, copies, and delivers every packet
Replaced
by OVS-DPDK in user space, or bypassed entirely
Completely bypassed
— NIC eSwitch handles L2 forwarding
Still active
— handles final delivery and all policy
KERNEL BYPASS
NONE
Full kernel stack active
FULL
Host + guest kernel bypassed
PARTIAL
Host hypervisor bypassed; guest kernel optional
NONE
Kernel stack fully active
THROUGHPUT
~20–40% of bare metal. Software bottleneck at high pps.
~90–95% of bare metal. 10–100 Gbps per dedicated core.
~97–99% of bare metal. Closest to native NIC performance.
~55–70% of bare metal. Better than standard; below SR-IOV.
CPU OVERHEAD
High — IRQ per packet, context switches, kernel copies
Dedicated core busy-polling; zero IRQ overhead on that core
Very low — host CPU not in data path; IOMMU handles DMA
Moderate — sorting offloaded; copy and delivery still on CPU
LIVE MIGRATION
FULL
Seamless, no interruption
PARTIAL
Requires OVS-DPDK; added complexity
RESTRICTED
VF detach/reattach causes brief interruption
FULL
No hardware binding; seamless migration
HARDWARE REQ.
Any NIC; no special requirements
Any DPDK-supported NIC; hugepages; dedicated CPU cores
SR-IOV NIC + IOMMU (VT-d/AMD-Vi) + SR-IOV BIOS enabled
Intel NIC with VMDq support; Intel-proprietary feature
OPEN STANDARD
YES
Linux kernel standard
YES
Linux Foundation open source
YES
PCI-SIG ratified standard
NO
Intel proprietary only
BEST FOR
General workloads; full vSwitch features; no performance requirement
NFV service chains; East-West traffic; OVS-DPDK; 5G UPF
North-South high throughput; telecom NFV; HFT; HPC
Enterprise VMware/Hyper-V; live migration required; moderate perf
Network I/O Virtualization Technologies
10 / 15
Notes: Now, let's look at a side-by-side comparison to clearly differentiate these technologies across key criteria. You'll notice that each method targets a different layer of overhead, leading to distinct performance characteristics and deployment scenarios. For instance, while SR-IOV offers the highest throughput, it comes with restrictions on live migration. DPDK, on the other hand, provides immense flexibility and programmability but demands dedicated CPU cores. VMDq strikes a balance, offering a performance boost while preserving full virtual switch features and live migration. Understanding these trade-offs is crucial, as the 'best' solution really depends on your specific workload requirements and infrastructure constraints. This comparison table should serve as a quick reference when evaluating your options. This brings us to our decision framework, which will help you choose the right technology for your needs.

## Slide 27
DECISION FRAMEWORK
Choosing the Right Technology Depends on Traffic Direction, Live Migration, and Hardware Constraints
SR-IOV
Single Root I/O Virtualization
CHOOSE SR-IOV WHEN…
North-South Throughput is the Priority
Traffic crosses server boundaries and you need the absolute closest performance to a bare-metal NIC. Telecom NFV, 5G UPF, and HPC interconnects are canonical use cases.
Host CPU Must Remain Free
The host CPU must not be consumed by packet processing. SR-IOV's hardware eSwitch and IOMMU DMA remove the host entirely from the data path.
Live Migration is Not a Hard Requirement
The operational model accepts brief network interruption during VM migration, or uses switchdev/SR-IOV live migration extensions to manage the transition.
SR-IOV-Capable Hardware is Available
The NIC, motherboard, and BIOS all support SR-IOV and IOMMU (Intel VT-d or AMD-Vi) is enabled. This is standard in modern server platforms.
DPDK
Data Plane Development Kit
CHOOSE DPDK WHEN…
East-West Traffic Dominates
Most traffic flows VM-to-VM on the same physical host. OVS-DPDK or VPP can switch this traffic in user space at line rate without leaving the server.
Programmable Packet Processing is Required
Custom forwarding logic, deep packet inspection, or NFV service chaining (vRouter → vFirewall → vLB) must be implemented in software with full control over the pipeline.
Standard Hardware Must Be Used
No SR-IOV hardware is available or the budget does not allow for specialised NICs. DPDK works on any commodity NIC with a supported Poll Mode Driver.
Combined with SR-IOV for Maximum Performance
SR-IOV delivers the VF to the VM, then DPDK inside the VM bypasses the guest kernel — creating a two-level bypass that achieves within 1% of bare-metal throughput.
VMDQ
Virtual Machine Device Queues
CHOOSE VMDQ WHEN…
Seamless Live Migration is Non-Negotiable
The operational model requires zero-interruption VM mobility between hosts. VMDq preserves full vSwitch compatibility and hypervisor control, enabling standard live migration.
vSwitch Features Must Be Preserved
Security groups, ACLs, port mirroring, and QoS policies must remain enforceable. VMDq keeps the hypervisor vSwitch in the path for all policy enforcement.
A Moderate Performance Improvement is Sufficient
The workload does not require SR-IOV-level throughput. Reducing hypervisor CPU load from packet sorting is sufficient to meet the performance target.
Intel NIC Hardware is Already Deployed
VMDq is available on existing Intel NIC deployments (82599, X710, E810 series) without additional hardware investment or BIOS reconfiguration.
COMBINED USAGE
SR-IOV
+
DPDK
+
VMDQ
A single physical server can run all three simultaneously: SR-IOV VFs assigned to latency-critical NFV workloads, OVS-DPDK switching East-West traffic between general VMs, and VMDq queues serving workloads that require live migration. The choice is not mutually exclusive at the server level — it is made per-workload and per-NIC-port.
Network I/O Virtualization Technologies
13 / 15
Notes: Choosing the right technology isn't about finding a single best solution; it's about matching the technology to your specific workload, traffic patterns, and operational needs. This decision framework helps clarify when to choose SR-IOV, DPDK, or VMDq. For example, if you need maximum North-South throughput and can tolerate live migration complexities, SR-IOV is your go-to. If your traffic is primarily East-West and you need highly programmable packet processing, DPDK is the answer. VMDq is ideal when you need a moderate performance boost without sacrificing live migration or existing virtual switch features. Remember, these aren't mutually exclusive choices. A single server can, and often does, run all three simultaneously, assigning different technologies to different virtual machines or network ports based on their unique requirements. With this framework in mind, let's summarise the key takeaways from our discussion.

## Slide 28
COMBINED USAGE
SR-IOV + DPDK: A Two-Level Bypass That Eliminates Both the Hypervisor and the Guest Kernel from the Packet Path
SR-IOV
DPDK
COMBINED PACKET PATH (RX)
Physical NIC + eSwitch
Hardware L2 forwarding by MAC/VLAN
VF DMA Ring
PCIe Virtual Function · Direct DMA
IOMMU / VT-d
Safe DMA address translation
Hypervisor vSwitch
Eliminated by SR-IOV
SR-IOV BYPASS
Guest Kernel NIC Driver
Eliminated by DPDK PMD
DPDK BYPASS
Guest TCP/IP Stack
Eliminated by DPDK PMD
DPDK BYPASS
DPDK Poll Mode Driver
User Space · Zero-copy · Hugepages
NFV Application
vRouter / vFirewall / 5G UPF
HOW THE TWO-LEVEL BYPASS WORKS
Level 1 — SR-IOV Eliminates the Hypervisor
SR-IOV exposes a hardware Virtual Function (VF) to the VM and the NIC's eSwitch delivers frames directly to the VF's DMA ring. The IOMMU translates addresses so the NIC DMA writes straight into guest memory. Result: no hypervisor packet processing or extra memory copies.
Level 2 — DPDK Eliminates the Guest Kernel
Inside the VM a DPDK PMD polls the VF's RX ring from user space, bypassing the guest kernel driver and TCP/IP stack. Packets land in DPDK hugepage mempools and are processed directly by the NFV app. Result: no guest IRQs or socket buffer copies.
Combined Result — Near Bare-Metal Performance
Together SR-IOV + DPDK remove software overhead between the NIC and the NFV application, typically yielding <1–3% throughput overhead versus bare metal. This is the recommended pattern for high-performance NFV deployments.
Operational Considerations
Requires SR-IOV capable NICs and IOMMU, DPDK hugepages, and a DPDK-compatible VF PMD. SR-IOV VF-bound VMs need special handling for live migration and monitoring.
PERFORMANCE
Typical overhead vs bare metal: <1–3% — SR-IOV removes the hypervisor layer; DPDK removes the guest kernel layer.
Network I/O Virtualization Technologies
10 / 15
Notes: We've explored each technology individually, but the real power often comes from combining them. This slide illustrates how SR-IOV and DPDK can work together to create a two-level bypass, effectively eliminating both the hypervisor and the guest kernel from the packet path. SR-IOV handles the first bypass, passing a virtual function directly to the VM, which means the hypervisor's virtual switch and memory management unit are completely removed from the data path. Then, inside the VM, a DPDK application takes over, using a poll mode driver to interact directly with that virtual function, bypassing the guest operating system's kernel. This combined approach results in a packet path with no software overhead from either the hypervisor or the guest kernel, achieving performance within one to three percent of bare metal. This architecture is the foundation for modern telecom network function virtualisation deployments, like virtual routers and 5G user plane functions. Next, let's put all these technologies side-by-side for a direct comparison.

## Slide 29
SUMMARY
Key Takeaways
01
Switching is never eliminated — only relocated
02
SR-IOV + DPDK is the NFV gold standard
03
All three are complementary, not competing
DETAILED TAKEAWAYS
01
Switching Is Never Eliminated — It Moves to a Different Layer
All three technologies bypass the software kernel vSwitch, but none remove the need for Layer 2 forwarding decisions. SR-IOV moves switching into the NIC eSwitch silicon, DPDK moves it into a user-space OVS-DPDK flow table, and VMDq offloads classification to NIC hardware queues while the vSwitch still delivers. MAC addresses and VLAN tags remain the universal addressing mechanism in all three cases.
SR-IOV ESWITCH
OVS-DPDK
VMDQ QUEUES
02
SR-IOV + DPDK Is the Gold Standard for NFV Data Plane Performance
Combining SR-IOV and DPDK creates a two-level bypass: SR-IOV removes the hypervisor vSwitch and VMM from the host data path, while DPDK inside the VM removes the guest kernel NIC driver and TCP/IP stack. The result is a packet path from physical NIC to NFV application with less than 1–3% overhead versus bare metal — the architecture recommended by Intel, Red Hat OpenStack, and the OKD/OpenShift NFV platform for 5G UPF, virtual routers, and virtual firewalls.
SR-IOV
DPDK
<1–3% OVERHEAD VS BARE METAL
03
The Three Technologies Are Complementary and Often Deployed Together
A single physical server can run all three simultaneously — SR-IOV VFs for latency-critical NFV workloads, OVS-DPDK for high-performance East-West VM-to-VM switching, and VMDq queues for workloads that require live migration and full vSwitch feature support. The choice is made per-workload and per-NIC-port, not as a single server-wide decision. VMDq and SR-IOV are mutually exclusive on the same port, but can coexist on different ports of the same NIC.
SR-IOV
DPDK
VMDQ
PER-WORKLOAD SELECTION
Network I/O Virtualization Technologies
14 / 15
Notes: To summarise, DPDK, SR-IOV, and VMDq are not competing technologies but rather complementary tools that address different aspects of virtualised networking performance. The core insight is that switching is never truly eliminated; it's simply relocated. SR-IOV moves it into the NIC's embedded switch, DPDK into a user-space flow table, and VMDq offloads classification to hardware queues. The combination of SR-IOV and DPDK represents the gold standard for network function virtualisation, providing a two-level bypass that achieves near bare-metal performance. This architecture is critical for demanding workloads like 5G user plane functions. Ultimately, a robust data center will likely deploy all three, leveraging each technology's strengths for specific workloads on the same physical server. This flexibility allows us to optimise performance across the entire virtualised environment. Finally, let's review the sources that informed this presentation.

## Slide 30
SOURCES AND FURTHER READING
References
10 SOURCES
1
SR-IOV for Network Function Virtualization Technology Brief
Intel Corporation
cdrdv2-public.intel.com/335625/sr-iov-nfv-tech-brief.pdf
2
Intel VMDq Technology White Paper
Intel Corporation
intel.com.tw/content/dam/www/public/us/en/documents/white-papers/vmdq-technology-paper.pdf
3
Intel Virtualization Technology for Connectivity (VT-c) Brief
Intel Corporation
intel.com/content/dam/support/us/en/documents/network/sb/intelvtcbrief.pdf
4
SR-IOV Architecture — Windows Hardware Developer Documentation
Microsoft Corporation
learn.microsoft.com/en-us/windows-hardware/drivers/network/sr-iov-architecture
5
About SR-IOV — Hardware Networks
Red Hat OpenShift Container Platform 4.18
docs.redhat.com/en/documentation/openshift_container_platform/4.18/html/hardware_networks/about-sriov
6
Using DPDK with SR-IOV — VM Networking
OKD / OpenShift
docs.okd.io/4.16/virt/vm_networking/virt-using-dpdk-with-sriov.html
7
DPDK vs SR-IOV for NFV: Why a Wrong Decision Can Impact Performance
TelcoCloudBridge
telcocloudbridge.com/blog/dpdk-vs-sr-iov-for-nfv-why-a-wrong-decision-can-impact-performance
8
An In-Depth Look at SR-IOV NIC Passthrough
vswitchzero.com
vswitchzero.com/2019/06/19/an-in-depth-look-at-sr-iov-nic-passthrough
9
Are VMDq and SR-IOV Performing the Same Function?
ITPro Today
itprotoday.com/server-virtualization/q-are-vmdq-and-sr-iov-performing-the-same-function
10
What is DPDK? Data Plane Development Kit Explained
Trenton Systems
trentonsystems.com/en-us/resource-hub/blog/what-is-dpdk
FEATURED SOURCE
Intel VT-c Technology Brief
Virtualization Technology for Connectivity — Intel's foundational document covering VMDq and SR-IOV hardware architecture, referenced as Source 3 above.
DISCLOSURE
All technical claims in this presentation are grounded in the primary sources listed. Performance figures are representative ranges drawn from vendor documentation and published benchmarks; actual results vary by hardware, workload, and configuration.
Network I/O Virtualization Technologies
15 / 15
Notes: Here you'll find a comprehensive list of references and further reading that informed this presentation. These sources include white papers from Intel, documentation from Microsoft and Red Hat, and articles from industry experts. I've also highlighted the Intel VT-c Technology Brief as a featured source, as it provides foundational insights into both VMDq and SR-IOV hardware architectures. It's important to note that while the performance figures discussed are representative, actual results can vary significantly based on your specific hardware, workload, and configuration. I encourage you to explore these resources for a deeper dive into the technical details of each technology. Thank you for your time and attention.